Shell Script for to add and mount new EBS volume when EC2 instance Disk usage reaches 50%

aws ec2 attach-volume --volume-id vol-0fff308d0b8c5589b --instance-id i-076fb38e6467f39e6 --device /dev/sda2
lsblk
mkfs.ext4 /dev/xvdf (for formating the disk)
mkdir -m 000 /vol (name should be equal to the name of volume in snapshot)
mount /dev/xvdb vol/
 df -h
cd /vol

mkdir /app
mount -t ext4 /dev/xvdf/app
df -h
cd /app
ds -ltr

Make an entry to /etc/fstab
Entry would be like:
/dev/sdf /data ext3 defaults 1 1
This will automatically mount the volume during reboot.
Commands to give output of memory usage , disk usage , cpu usage

free -m | awk 'NR==2{printf "Memory Usage: %s/%sMB (%.2f%%)\n", $3,$2,$3*100/$2 }'

df -h | awk '$NF=="/"{printf "Disk Usage: %d/%dGB (%s)\n", $3,$2,$5}'

top -bn1 | grep load | awk '{printf "CPU Load: %.2f\n", $(NF-2)}'

#!/bin/bash

echo " Write in your age: "
read age

if [[ "$age" -le 7 || "$age" -ge 65 ]] ; then
    echo " You can walk in for free "
elif [[ "$age" -gt 7 && "$age" -lt 65 ]] ; then
    echo " You have to pay for ticket "
fi

#!/bin/bash

TOTAL_DISK_USAGE="$(df -h | awk '$NF=="/"{printf "%s\n", $5}')"
DISK_USAGE_THRESHOLD="23%"

if [ "$DISK_USAGE_THRESHOLD" \< "$TOTAL_DISK_USAGE" ] ; then
  echo overexide
  aws ec2 attach-volume --volume-id vol-0fff308d0b8c5589b --instance-id i-076fb38e6467f39e6 --device /dev/sda2
  lsblk
  mkfs.ext4 /dev/xvdf
  mkdir -m 000 /vol
  mount /dev/xvdb vol/
  df -h
  cd /vol
else
  echo $TOTAL_DISK_USAGE ------- $DISK_USAGE_THRESHOLD
  echo Not required extra disk
  exit 0

fi

#!/bin/bash
VOL_DATA="$(aws ec2 create-volume --size 1 --region us-east-1 --availability-zone us-east-1a --volume-type gp2)"

echo "wait for 20s"

sleep 20s

echo $VOL_DATA

sleep 5s

read -p "VOLUME ID: " vol

echo $vol

============Shell Script which is working correctly===========
 #!/bin/bash

TOTAL_DISK_USAGE="$(df -h | awk '$NF=="/"{printf "%s\n", $5}')"
DISK_USAGE_THRESHOLD="11%"

if [ "$DISK_USAGE_THRESHOLD" \< "$TOTAL_DISK_USAGE" ] ; then
  VOL_DATA="$(aws ec2 create-volume --size 1 --region us-east-1 --availability-zone us-east-1a --volume-type gp2)"
  echo "wait for 20s"
  sleep 20s
  #echo $VOL_DATA
  #sleep 5s
  VID=$(echo "$VOL_DATA" | jq '.VolumeId' )
  echo $VID
  echo overexide
  id="$(aws ec2 describe-instances --filters Name=tag:Name,Values="lucky" --query 'Reservations[].Instances[].InstanceId' --output text)"
  aws ec2 attach-volume --volume-id $vol --instance-id $id --device /dev/sda2
  lsblk
  sleep 20s
  mkfs.ext4 /dev/xvdb
  mkdir -m 000 /vol
  mount /dev/xvdb /vol
  df -h
  cd /vol
else
  echo $TOTAL_DISK_USAGE ------- $DISK_USAGE_THRESHOLD
  echo Not required extra disk
  exit 0

fi

================Using jq for filtering VolumeId and puting in variable===========

#!/bin/bash
VOL_DATA='{ "Iops": 100, "VolumeId": "vol-026cace65e9d67ebc", "SnapshotId": "", "AvailabilityZone": "us-east-1a", "Size": 1, "CreateTime": "2018-03-20T11:27:04.411Z", "State": "creating", "VolumeType": "gp2", "Encrypted": "xyz" }'
echo "wait for 20s"
sleep 1s

ID=$(echo "$VOL_DATA" | jq '.VolumeId' )
echo $ID

======================This one is also working =================

#!/bin/bash

TOTAL_DISK_USAGE="$(df -h | awk '$NF=="/"{printf "%s\n", $5}')"
DISK_USAGE_THRESHOLD="11%"

if [ "$DISK_USAGE_THRESHOLD" \< "$TOTAL_DISK_USAGE" ] ; then
  VOL_DATA="$(aws ec2 create-volume --size 1 --region us-east-1 --availability-zone us-east-1a --volume-type gp2)"
  echo "wait for 20s"
  sleep 20s
  VID=$(echo "$VOL_DATA" | jq '.VolumeId' | sed -e 's/^"//' -e 's/"$//')
  echo $VID
  echo overexide
  id="$(aws ec2 describe-instances --filters Name=tag:Name,Values="lucky" --query 'Reservations[].Instances[].InstanceId' --output text)"
  #instanceid="$(curl http://169.254.169.254/latest/meta-data/instance-id)"
  echo $id
  aws ec2 attach-volume --volume-id $VID --instance-id $id --device /dev/sda2
  lsblk
  sleep 20s
  mkfs.ext4 /dev/xvdb
  mkdir -m 000 /vol
  mount /dev/xvdb /vol
  df -h
  cd /vol
else
  echo $TOTAL_DISK_USAGE ------- $DISK_USAGE_THRESHOLD
  echo Not required extra disk
  exit 0

fi